## Slide 1
SMART MMU (SMMU) Design Module Overview
Flexible Shared SRAM Address Management Module
Project: 4-Port 2.5G/1G/100M Ethernet Switch
Clock Domain: clk_core, 300 MHz Single Clock Domain
Date: July 16, 2026
CONFIDENTIAL TECHNICAL REVIEW
Simplified Block Diagram of the Main Packet-Processing Path

## Slide 2
AGENDA
01
Design Context and Positioning
02
Top-Level Architecture and Module Partitioning
03
Data Structures (Cells / Linked Lists / Dual Pools)
04
Workflows (Initialization / Enqueue / Dequeue, etc.)
05
Multicast
06
Aging
07
08
Summary
SMMU Design Review
Flow Control (PAUSE / PFC)

## Slide 3
Design Context — MMU in the Switch ASIC
Core Responsibilities and Positioning
The MMU is the address-management submodule of the QM (Queue Manager). It centrally allocates addresses and organizes linked lists for the 2 MB shared data SRAM at a granularity of 256-byte cells.
Capacity Derivation
Item
Value
Description
Shared Data SRAM
2 MB
Packet payload buffer
Cell Granularity
256 B
Minimum management unit
Total Cells
8192
2MB / 256B
Address Width
13 bit
$clog2(8192)
Data Plane (Payload) vs. Address Plane Comparison
QM/EPS moves the data; SMMU only allocates and reclaims 256-byte cell addresses (pointers) and manages their linked lists.
SMMU Design Review

## Slide 4
Linked Lists vs. Static Partitioning
Static Partitioning
Low utilization: idle cells cannot be borrowed across queues.
Inflexible: changing queue quotas requires repartitioning physical addresses.
Fragmentation: scattered free space cannot be utilized.
•
•
•
Linked-List Approach
Fully shared: any cell can be assigned to any queue, approaching 100% utilization.
O(1) complexity: enqueue and dequeue update only head and tail pointers.
Native dual pools: reserved guarantees plus dynamic sharing.
•
•
•
SMMU Design Review

## Slide 5
Core Design Constraints
1. Maximum Performance
Enqueue and dequeue complete in exactly one cycle (request at T0, result at T1), sustaining back-to-back throughput of one cell per cycle.
2. Unicast and Multicast
Supports both unicast and multicast. Multicast uses one shared data copy across multiple ports and reclaims storage automatically through reference counting.
3. Flow Control
Supports PAUSE (802.3x) and PFC (802.1Qbb), with per-queue, per-port, and global max/near-full feedback for enqueue gating.
4. Storage Optimization
Linked-list pointers reside in Next-Ptr SRAM. Two-stage prefetch registers absorb the one-cycle read latency and keep the pipeline running without stalls.
5. Dual Buffer Pools
A statically reserved pool (per-queue guarantee) plus a dynamically shared pool balances QoS fairness with buffer utilization.
6. Configuration Plane
CSRs bypass a slow bus. Configuration signals are sampled directly in the clk_core domain for immediate updates and simpler integration.
SMMU Design Review

## Slide 6
Top Level Arch
Core:
Seven modules center on
LLE (Link-List Engine)
and link via
occ_query
,
alloc_fire
to decouple control and storage planes.
Submodule
Plane
Primary Responsibility
LLE
M
Linked-list engine; sole accessor of Next-Ptr SRAM
enqueue_ctrl
Ctrl
One-cycle enqueue command; whole-frame drop FSM
dequeue_ctrl
Ctrl
One-cycle dequeue command; backpressure check
recycle_ctrl
Ctrl
Thin pass-through for returning cells to the free list
occupancy_mgr
Cnt
Occupancy counters + dual-pool decision + PAUSE/PFC
aging_ctrl
Ctrl
Queue aging flush to prevent zombie queues
csr_stats_init
Cfg
Configuration sampling + initialization FSM (free-list construction)
Inter-Module Interface Conventions:
All control modules allocate and release addresses through the LLE
The Occupancy module provides real-time watermarks for enqueue gating
The Init FSM builds the linked list in Next-Ptr SRAM after power-up
SMMU Design Review

## Slide 7
Parameterized Design
All widths are derived consistently from CELL_NUM, PORT_NUM, and TC_NUM across all submodules, ensuring design consistency and scalability.
Top-Level Parameters
Parameter
Default
Description
CELL_NUM
8192
Total cells (2 MB / 256 B)
PORT_NUM
4
Number of physical egress ports
TC_NUM
8
Traffic classes per port
STAT_W
32
Statistics counter width
Derived Constants (Localparams)
Derived Value
Expression
Value (Default)
QUEUE_NUM
PORT*TC+1
33
ADDR_W
$clog2(CELL)
13
QID_W
$clog2(QN)
6
PORT_W
$clog2(PN)
2
CNT_W
ADDR_W+1
14
SMMU Design Review
REF_W
PORT_W
2
PKT_CELL_W
4
Packet cell number width

## Slide 8
LLE Linked List
Physical Implementation: Next-Ptr SRAM
The linked list is stored in Next-Ptr SRAM, which records the successor pointer for every cell.
Parameter
Specification
Memory Depth
8192 (CELL_NUM)
Data Width
13 bit (ADDR_W)
Interface Type
1R1W (independent read/write ports)
Read Latency
1 cycle (absorbed by prefetch registers)
Head/Tail Pointer Registers
q_head[33]: points to the first cell address of each queue.
q_tail[33]: points to the last cell address of each queue.
free_head/free_tail: maintain the head and tail of the free-address pool.
q_cell_cnt[33], free_cell_cnt: Counter of cell number.
All pointers are implemented as registers for single-cycle access and update.
Operations and Free-List Maintenance
Enqueue
Pop an address from free_head, append it after the target queue's q_tail, and update that queue's tail pointer.
Dequeue
Pop the address at q_head and update the head with next_ptr read from SRAM. On reclamation, append the released address to free_tail.
Free List
At initialization, all 8,192 unused cells form one long singly linked list, enabling O(1) address allocation.
SMMU Design Review

## Slide 9
Dual-Pool Buffer Management
Mechanism
Reserved Pool: guarantees capacity for each queue so basic forwarding remains available under congestion and QoS starvation is prevented.
Shared Pool: all active queues dynamically compete for the remaining buffer, greatly improving absorption of burst traffic.
Allocation Decision Logic
// Prefer reserved capacity use_reserved = (q_usage < q_min); // Request shared capacity after the reserve is exhausted use_shared = (q_usage >= q_min) && (shared_usage < shared_limit);
Dual-Pool Watermarks and Thresholds
Configurable q_min (guarantee) and shared_limit (shared cap) enable fine-grained buffer-resource scheduling.
SMMU Design Review

## Slide 10
Process — CSR
CSR Configuration Interface
The CPU can adjust core parameters in real time, including flow-control thresholds (XOFF/XON), dual-pool reserve ratios, and the aging-timer period, enabling dynamic performance tuning.
Performance Monitoring and Statistics
• Real-time counters: accurately track total enqueued/dequeued packets and dropped cells. • Watermark tracking: sample peak queue and global buffer occupancy in real time. • Exception reporting: interrupt system software on SRAM ECC errors, illegal address accesses, and other faults.
CSR and Statistics Module Architecture
Strong observability provides solid data support for system debugging and performance tuning.
SMMU Design Review

## Slide 11
Process — Power-Up Init FSM
Init FSM State Transitions
•
IS_IDLE: wait for reset release or init_start↑.
•
IS_BUILD: LLE builds the free list, one link per cycle.
•
IS_DONE
: assert init_done and enter Ready.
Automatic List Construction in the LLE
•
Write
: write SRAM[idx].next = idx + 1 each cycle.
•
Self-Loop
: last cell.next points to itself, marking the list end.
•
Reg Sync
: init pointers and prefetch; allocate on cycle one.
Automatic Next-Ptr SRAM List Construction
Hardware initialization makes the free list deterministic and brings the system to Ready quickly after power-up.
SMMU Design Review

## Slide 12
Process — Enqueue
T0/T1 Timing and Handshake
•
T0
: accept enq_req; Occupancy returns a same-cycle decision.
•
T1
: register alloc_valid and alloc_cell_addr, providing an exact
one-cycle command response.
Tail-in-Register Linking
•
Relink Delay
: keep q_tail_q in a register; defer
SRAM[old_tail].next = new_cell until
the next enqueue.
•
Benefits
: no write for empty links; ≤1 write/cycle; tail in reg.
Enqueue Linking (A→B→C): Register and SRAM Evolution
Caching the tail in a register enables efficient list appends and deterministic SRAM access timing.
SMMU Design Review

## Slide 13
Process — Whole-Frame Drop
1. Predictive Watermark Logic
When the first cell (SOF) of a packet arrives, the system predicts occupancy from packet length instead of deciding cell by cell.
predict_occ = current_occ + pkt_cell_num;
This up-front prediction prevents packet truncation caused by buffer exhaustion mid-frame.
2. Whole-Frame Drop Policy
If predicted occupancy exceeds the configured threshold, Early Drop is triggered:
• Accept all or drop all: all cells of a packet receive the same disposition. • Resource protection: prevents fragmented packets from consuming valuable SRAM capacity.
3. FSM State Control
enqueue_ctrl
maintains the enqueue state machine:
• IDLE: wait for an SOF request. • DROP: prediction fails; discard subsequent cells through EOF. • ACCEPT: prediction passes; accept subsequent cells through EOF.
SMMU Design Review

## Slide 14
Process — Dequeue
Dequeue Logic and Handshake
•
T0
: deq_req; check BP/non-empty; address = lle_qhead.
•
T1
: output deq_cell_valid/deq_cell_addr after exactly one cycle.
Three-Stage Prefetch Register Scheme
•
Window
: head/next/next2 slide forward on each dequeue.
•
Refill
: if len≥3, background-read next2.
•
Gain
: absorbs SRAM latency; line-rate back-to-back dequeue.
Queue-Head Sliding Window
The head address is always visible in a register, so the dequeue address is available immediately without waiting for an SRAM read response.
SMMU Design Review

## Slide 15
Process — Two-Stage Prefetch
Design Challenge
Next-Ptr SRAM has a one-cycle read latency. During continuous dequeue, waiting for the next pointer would create pipeline bubbles and prevent full throughput.
Solution
Prefetch Reg 0 and Prefetch Reg 1 form a two-stage prefetch pipeline:
• Issue read requests for subsequent cell addresses in advance. • Cache returned pointers in registers to absorb SRAM latency completely. • Sustain back-to-back dequeue performance.
LLE Prefetch Pipeline Architecture
The two registers ensure that the LLE always has the next valid address available.
SMMU Design Review

## Slide 16
Process — Recycle
Reclamation Paths
•
Unicast
: push directly to the free list and decrement the
queue count.
•
Multicast
: decrement the reference count on each return;
push only when the count reaches zero.
•
Thin Path
:
recycle_ctrl
is a type-independent interface;
the LLE handles the difference internally.
Two-Stage Symmetric Reclamation
•
Stage 1
: address → FIFO;
free_cnt
++ now
(logically free).
•
Stage 2
: on FIFO pop, write
SRAM[old_tail].next = X
→
free_tail_q
.
•
Sym.
: same Tail-in-Register method as enqueue;
keeps SRAM writes ordered.
Two-Stage Address Reclamation
Reclamation and enqueue share the same tail-register handling, greatly simplifying SRAM access arbitration.
SMMU Design Review

## Slide 17
Process — LLE Arbitration
As the sole module accessing Next-Ptr SRAM, the LLE (Link-List Engine) coordinates requests from multiple control planes through efficient arbitration.
Arbitration Priority
Priority
Operation
Design Rationale
H
Dequeue
Prevents address-read stalls at the transmitter and preserves line-rate forwarding.
M
Enqueue
Uses idle slots for writes; packet-level enqueue locking preserves atomicity.
L
Recycle
FIFO
SRAM Time-Division Multiplexing
Single-Port SRAM
: TDM arbitration makes a single-port SRAM appear to
support multiple concurrent requesters.
Conflict
: simultaneous requests are resolved by priority, and losing requests
retry in the next cycle.
Pipeline
: the arbitration result directly drives the SRAM address lines;
prefetch registers enable seamless switching.
SMMU Design Review

## Slide 18
Flow Control — Drop
1. Queue-Level Feedback
q_max_reached[33]
: high queue level; QM applies WRED or gating.
Prevents queue monopolization.
2. Port-Level Feedback
port_max_reached[4]
: aggregate port level; triggers port PAUSE.
Backpressures peer.
3. Global-Level Feedback
global_max_reached
: critical SRAM level; global PAUSE prevents overflow.
Low-Latency Feedback Path
The Occupancy module drives decisions directly to QM, bypassing complex bus arbitration so flow control takes effect within 1–2 cycles and minimizes packet loss.
SMMU Design Review

## Slide 19
Flow Control — PAUSE/PFC Hysteresis
Decision Logic
XOFF (Stop): assert PAUSE when buffer occupancy rises above the high threshold, instructing the peer to stop transmitting.
XON (Resume): deassert PAUSE only after occupancy falls below the low threshold, allowing the peer to resume.
Benefits of Hysteresis
Setting XOFF > XON creates a hysteresis band between the thresholds. This prevents frequent oscillation near the threshold and stabilizes the control plane.
PAUSE/PFC Hysteresis Control
The hysteresis band absorbs traffic fluctuations, reduces control-frame frequency, and improves link efficiency.
SMMU Design Review

## Slide 20
Multicast — Overview
Single-Slot Model
To simplify hardware implementation, SMMU uses a single-slot processing model.
Only one multicast frame is stitched at a time, keeping state-machine transitions deterministic and efficient.
Zero Copy
The primary goal is storage conservation.
A multicast frame has only one physical copy in Next-Ptr SRAM. Multiple logical pointers read that copy concurrently, substantially reducing buffer consumption.
Logical Stitching
Multicast data does not form a separate linked list; it is logically stitched into the unicast flow.
From QM's perspective, multicast frames transparently interleave with the unicast queue, enabling seamless integration with existing service logic.
SMMU Design Review

## Slide 21
Multicast — Enqueue
Key State Registers
Register
Function
mc_dst_bitmap_q
mc_alloc_mcast_tc
Destination-port bitmap recording every physical port targeted by the multicast frame.
mc_valid_q
Multicast-slot valid flag; indicates whether the current B2 slot contains a multicast frame.
mc_cells_q[16]
Mirror of the frame's cell-address list, allowing each port to read the complete multicast frame.
mc_rd_idx_q[4]
Per-port private read pointers advance independently.
mc_pend_uni_q[4]
Per-port pending-unicast flag indicating that the port is still processing a preceding unicast frame.
SMMU Design Review

## Slide 22
Multicast — Private Pointers
Mechanism
Each destination port has an independent mc_rd_idx_q[p] register.
Port A may be reading cell 2 while backpressured port B is still on cell 1. This decoupling preserves per-port independence.
Key Benefits
• One copy, multiple readers: SRAM stores only one packet copy. • Zero-copy forwarding: no per-destination duplication, saving internal bandwidth and storage. • Independent pacing: a slow port does not block a fast port's read progress.
B2 Multicast Private-Read-Pointer Model
Per-port private read pointers provide logically concurrent access to a single physical copy.
SMMU Design Review

## Slide 23
Multicast — Dequeue
Stitching Trigger Conditions
1. Unicast Frame Dequeue Completes
When the port's preceding unicast frame is fully transmitted (mc_pend_uni_q[p] == 0), the stitching check is triggered.
2. Multicast Slot Is Ready
The multicast slot is valid (mc_valid_q == 1) and the port is set in the destination bitmap (mc_dst_bitmap_q[p] == 1).
3. Read Pointer Is In Range
mc_rd_idx_q[p] is below the frame's cell count.
QM Perspective and Transparent Processing
Transparency: QM always sees an ordinary unicast queue. Internally, SMMU inserts multicast cells between unicast frames through logical selection.
Seamless switching: once stitching conditions are met, the LLE switches from the SRAM linked list to the multicast mirror registers mc_cells_q with zero added latency.
SMMU Design Review

## Slide 24
Multicast — Ref-Count Recycle
SMMU Design Review

## Slide 25
Aging — Zombie Cleanup
SMMU Design Review

## Slide 26
Design Highlights
High-Throughput Pipeline
Strict 1-cycle enqueue/dequeue (T0 request → T1 result)
Back-to-back operation: one cell per clock, no stalls
Two-level prefetch fully absorbs the Next-Ptr SRAM read latency
Dual-Pool Buffering & Flow Control
Static reserved pool (guaranteed) + dynamic shared pool (high utilization) — fair yet efficient
Admission drop decision at enqueue (queue / port / global / shared-pool limits)
Whole-frame pre-check and whole-frame drop (no half-linked packets)
IEEE 802.3x PAUSE & 802.1Qbb PFC with XOFF/XON dual-threshold hysteresis
Zero-Copy Multicast
Single slot: one multicast frame in flight at a time
Zero copy: one shared linked list in SRAM, no per-port duplication
Per-port private read pointers: independent pacing, no head-of-line blocking
Reference-count recycle: cell freed only after every destination port has sent it
Autonomous Aging
MMU self-detects zombie queues (occupied but long unserved)
Round-robin scanner flushes one queue at a time, fairly
Cells auto-recycled to the free list; QM notified to sync its bookkeeping
SMMU Design Review

## Slide 27
Conclusion
Thank You
Q & A
Smart MMU (SMMU) Design Module Overview | 2026