## Slide 1
Specification
Verilog/VHDL
Party EDIF
XDC Constraints
.v/.sv/.vhd
.edn
.xdc
Save Design Checkpoint at each stage(.dcp)
Vivado System Builder
IP,DSP,uP
Elaborate
Synth_design
Report_timing_summary
Opt_design
Power_opt_design
Place_design
Power_opt_design
Phys_opt_desgin
Route_design
Report_timing_summary
Write_bitstream
Behavioral Simulation
Timing Simulation

## Slide 2
RTL System-Level Integration
DSP Design
(System Genetator)
IP Integration
(Embedded,Logic,DSP…)
IP Packaging
Customer IP
RTL
EDIF
XDC
IP Catalog
Xilinx IP
IP
User IP
Synthesis
Design Analysis
Constraints
Simulation
Debugging
Cross Probing
Programming & Debug
Implementation

## Slide 3
src
edn
ip
xdc
sysgen
sim
Vivado
Project Mode
Project_name.xpr
Project_name.runs
Project_name.srcs
Project_name.data
Non-Project Mode
.dcp
.rpt
GUI Tcl
Tcl

## Slide 4
IP
Instantiation Template
Synthesized Checkpoint
Behavioral Simulation
<ip_name>_funcsim.v/vhdl
<ip_name>_stub.v
<ip_name>.vho
Example Design
Testbench
.veo
.vho
.dcp
.v
.vhdl
For Simulation Tool
For Synthesis Tool

## Slide 5
IP Packager
User IP
Party IP
Xilinx IP
IP Catalog
User
Design
Source（RTL,IP,etc）
Simulation Module
Doc
Example Design
Testbench
Customer
RTL Code

## Slide 6
RTL Design
Synthesize
Implement
Debug the Design
Behavioral Simulation
Verify Design Behaves as Intended
Post Synthesis Simulation
Verify the synthesized design meets the functional requirements and behaves as expected
Post Implementation Simulation
Closest emulation to HW